## Slide 1: Single and Parallel Machine Scheduling
IE 419
Supplementary Reference:
M. Pinedo, “Scheduling: Theory, Algorithms, and Systems, 3rd Ed.”, Springer, 2008
http://users.utu.fi/yurnik/scheduling_files/Scheduling.Theory,.Algorithms,.and.Systems_Michael_Pinedo.pdf
http://www.ebook3000.com/Scheduling--Theory--Algorithms--and-Systems_22332.html

## Slide 2: Modeling Parameters
Typical scheduling parameters:
Number of resources (m machines, operators)
Configuration and layout
Resource capabilities
Number of jobs (n)
Job processing times (pij)
Job release and due dates (resp. rij and dij )
Job weight (wij ) or priority
Setup times

## Slide 3: Decision Outcomes
Three basic types of solutions:
  A sequence: a permutation of the jobs
  A schedule: allocation of the jobs in a more complicated setting of the environment
  A scheduling policy: determines the next job given the current state of the system

## Slide 4: Emphasis on Completion time
1
1
1
1
2
2
2
3
3
3
4
4
4
Resources
2
3
Time
C2, C3
C1
C4

## Slide 5
Optimality criteria
We define for each job j:
Cij completion time of the operation of job j on machine i
Cj time when job j exits the system
Lj = Cj - dj lateness of job j
Tj = max(Cj - dj , 0) tardiness of job j
unit penalty of job j

## Slide 6
Possible objective functions to be minimised:
Makespan Cmax - max (C1,...,Cn)
Maximum lateness Lmax - max (L1,...,Ln)
Total weighted completion time  wjCj - weighted flow time
Total weighted tardiness  wjTj
Weighted number of tardy jobs  wjUj
Optimality criteria
Flowtime
  Time job j spends in the system
  Flow time: Fj = Cj - rj
1) Minimize average flowtime
2) Minimize maximum flowtime

## Slide 7: Due Date Penalties
In practice
Tardiness
Late or Not
Lateness

## Slide 8
Generic notation of scheduling problem
for example:
Pm | rj, prmp | ΣwjCj (parallel machines)
1 | sjk | Cmax (sequence dependent
setup / traveling salesman)
Q2 | prec | ΣwjTj (2 machines w. different speed, precedence constraints, weighted tardiness)
Scheduling problem:  |  | 
 machine environment
 job characteristics
 optimality criteria

## Slide 9
Single Machine Deterministic Models
Jobs: J1, J2, ..., Jn
Assumptions:
The machine is always available throughout the scheduling period.
The machine cannot process more than one job at a time.
Each job must spend on the machine a prescribed length of time.

## Slide 10: Optimal Solution
Lets say we have
  Single machine (1), where
  the total weighted completion time should be minimized (SwjCj)
Theorem: Weighted Shortest Processing time first - called the WSPT rule -
Note: The SPT rule starts with the job that has the shortest processing time, moves on the job with the second shortest processing time, etc.

## Slide 11: Proof (by contradiction)
Suppose it is not true and schedule S is optimal
Then there are two adjacent jobs, say job j followed by job k such that
Do a pairwise interchange to get schedule S ’
j
k
k
j

## Slide 12: Proof (continued)
The weighted completion time of the two jobs under S is
The weighted completion time of the two jobs under S ’ is
Now:
Contradicting that S is optimal.

## Slide 13
WSPT Example
Find all optimal sequences for the scheduling problem 1 || wjCj with the following jobs.

## Slide 14
WSPT Example Answer
jobs 1 2 3 4 5 6 7
wj 0 18 12 8 8 17 16
pj 3 6 6 5 4 8 9
wj /pj 0 3 2 1.6 2 2.125 1.78
jobs 2 6 3 5 7 4 1
wj 18 17 12 8 16 8 0
Cj 6 14 20 24 33 38 41
wjCj = 1610
or
jobs 2 6 5 3 7 4 1
wj 18 17 8 12 16 8 0
Cj 6 14 18 24 33 38 41
wjCj = 1610

## Slide 15
1 | chain | wjCj
chain 1: 1  2  ...  k
chain 2: k+1  k+2  ...  n
Lemma. If
the chain of jobs 1,...,k precedes the chain of jobs k+1,...,n.
Let l* satisfy
 factor of chain 1,...,k
l* is the job that determines the  factor of the chain

## Slide 16
Lemma. If job l* determines  (1,...,k) , then there exists an optimal sequence that processes jobs 1,...,l* one after another without interruption by jobs from other chains.
Algorithm
Whenever the machine is free, select among the remaining chains the one with the highest  factor.
Process this chain up to and including the job l* that determines its  factor.
1 | chain | wjCj

## Slide 17
Example
chain 1: 1  2  3  4
chain 2: 5  6  7
 factor of chain 1 is determined by job 2: (6+18)/(3+6)=2.67
 factor of chain 2 is determined by job 6: (8+17)/(4+8)=2.08
chain 1 is selected: jobs 1, 2
 factor of the remaining part of chain 1 is determined by job 3: 12/6=2
 factor of chain 2 is determined by job 6: 2.08
chain 2 is selected: jobs 5, 6
1 | chain | wjCj

## Slide 18
 factor of the remaining part of chain 1 is determined by job 3: 2
 factor of the remaining part of chain 2 is determined by job 7: 18/10=1.8
chain 1 is selected: job 3
 factor of the remaining part of chain 1 is determined by job 4: 8/5=1.6
 factor of the remaining part of chain 2 is determined by job 7: 1.8
chain 2 is selected: job 7
job 4 is scheduled last
the final schedule: 1, 2, 5, 6, 3, 7, 4
1 | chain | wjCj

## Slide 19
P and NP problems
The efficiency of an algorithm for a given problem is measured by the maximum (worst-case) number of computational steps needed to obtain an optimal solution as a function of the size of the instance.
Problems which have a known polynomial algorithm are said to be in class P.
These are problems for which an algorithm is known to exist and it will stop on the correct output while effort is bounded by a polynomial function of the size of the problem.
For NP (non-deterministic polynomial problems) no simple algorithm yields optimal solutions in a limited amount of computer time.

## Slide 20
“Hard” Single Machine Problems
Polynomial time algorithms for more complex precedence constraints than the simple chains are developed.
The problems with arbitrary precedence relation are NP hard.
1 | rj, prmp | wjCj preemptive version of the WSPT rule does not always lead to an optimal solution, the problem is NP hard
1 | rj, prmp | Cj preemptive version of the SPT rule is optimal
1 | rj | Cj is NP hard

## Slide 21
1 || Lmax is the special case of the 1 | prec | hmax
where hj = Cj – dj
hj are nondecreasing cost functions
hmax = max ( h1(C1), ... ,hn(Cn) )
  Algorithm results in the schedule that orders jobs in increasing order of their due dates - earliest due date first rule (EDD)
1 | rj | Lmax is NP hard , branch-and-bound is used
1 | rj , prec | Lmax similar branch-and-bound
Lateness Models

## Slide 22: Hard vs Easy
Easy:
  Sort n numbers
  Solve a system of linear equations
Hard:
  Schedule a factory, deliver packages, schedule buses
f (n): the number of “basic operations” needed to solve the problem with input size n
Easy: f (n) is polynomial in n
  O(n), O(n log n), O(n2), …
Hard: f (n) is exponential in n
  O(2n), …
The complexity of an algorithm is its running time in terms of the input parameters (e.g., number of jobs and number of machines)

## Slide 23: Polynomial versus NP-Hard

## Slide 24: Hard vs Easy
O(n) | O(n log n) | O(n2) | O(2n)
1 | 0 | 1 | 2
10 | 10 | 100 | 1024
20 | 26 | 400 | 1048576
50 | 85 | 2500 | 1,125,899,906,842,624
100 | 200 | 10000 | 1.268 X 1030
1000 | 3000 | 1,000,000 | 1.072 X 10301

## Slide 25: Hard vs Easy
10301 operations required in worst case
Age of universe: 1018 seconds
Fastest Computer today: 1014 op/sec
Let’s say we get a computer 1018 times faster (a sextillion times faster)
  1033 op/sec
It may still take 10250 times longer than the age of the universe to solve the problem!

## Slide 26
1
2
3
0 5 10 15
EDD
Can we
improve?

## Slide 27: Delay Schedule
1
2
3
0 5 10 15
Add a delay
What makes this problem hard is that
the optimal schedule is not necessarily
a “non-delay” schedule

## Slide 28: Final Classic Result
The preemptive EDD rule is optimal for the preemptive (prmp) version of the problem
Note that in the previous example, the preemptive EDD rule gives us the optimal schedule

## Slide 29: Branch and Bound
The problem
cannot be solved using a simple dispatching rule so we will try to solve it using branch and bound
To develop a branch and bound procedure:
  Determine how to branch
  Determine how to bound
Enumerative method
Guarantees finding the best schedule
Basic idea:
  Look at a set of schedules
  Develop a bound on the performance
  Discard (fathom) if bound worse than best schedule found before

## Slide 30
Branch-and-bound algorithm
Search space can grow very large as the number of variables in the problem increases!
Branch-and-bound is a methodology that works on the idea of successive partitioning of the search space.
S
S1
S2
Sn
S12
S13
. . .
. . .
. . .
S = S1 S2... Sn
S1 S2 ...  Sn = 

## Slide 31
S
S1
S2
Sn
S12
S13
. . .
. . .
We need some means for obtaining a lower bound on the cost for any particular solution (the task is to minimise the cost).
fbound  f(x), xS1
  fbound  f(x), xS2
there is no need to explore S2
Branch-and-bound algorithm
Best feasible solution
found, so far…

## Slide 32
*,*,*,*
1,*,*,*
2,*,*,*
n,*,*,*
1,2,*,*
1,3,*,*
. . .
. . .
. . .
Branch-and-bound algorithm for 1 | rj | Lmax
Solution space contains n! schedules (n is number of jobs).
Total enumeration is not viable !

## Slide 33: Data

## Slide 34
Branching rule:
k level, j1, ... , jk are scheduled,
A job j* needs to be considered if no job still to be scheduled can not be processed before the release time of job j*
  that is:
J set of jobs not yet scheduled
t is time when jk is completed
*,*,*,*
1,*,*,*
2,*,*,*
n,*,*,*
1,2,*,*
1,3,*,*
. . .
. . .
. . .
1st level
2nd level
Branch and Bound

## Slide 35
Branching
(•,•,•,•)
(1,•,•,•)
(2,•,•,•)
(3,•,•,•)
(4,•,•,•)
Discard immediately because

## Slide 36
Branching
(•,•,•,•)
(1,•,•,•)
(2,•,•,•)
(3,•,•,•)
(4,•,•,•)
Need to develop lower bounds on
these nodes and do further branching.

## Slide 37: Bounding (in general)
Typical way to develop bounds is to relax the original problem to an easily solvable problem
Three cases:
  If there is no solution to the relaxed problem there is no solution to the original problem
  If the optimal solution to the relaxed problem is feasible for the original problem then it is also optimal for the original problem
  If the optimal solution to the relaxed problem is not feasible for the original problem it provides a bound on its performance

## Slide 38: Relaxing the Problem
The problem
is a relaxation to the problem
Not allowing preemption is a constraint in the original problem
  but not the relaxed problem
We know how to solve the relaxed problem
  preemptive EDD rule
Preemptive EDD rule optimal for the preemptive version of the problem
Solution obtained is a lower bound on the maximum delay
If preemptive EDD results in a non-preemptive schedule all nodes with higher lower bounds can be discarded.

## Slide 39
Example
Non-preemptive schedules
0
1
2
3
7
12
2
1
0
5
9
L1=3
L2=6
Lmax=6
L1=5
L2=-1
Lmax=5
Preemptive schedule obtained using EDD
2
1
2
0
3
7
9
L1=3
L2=3
Lmax=3
the lowest Lmax !

## Slide 40: Lower Bounds
Start with (1,•,•,•):
  Job with EDD is Job 4 but
  Second earliest due date is for Job 3
Job 1
Job 2
Job 3
Job 4
0 10 20

## Slide 41
Branching
(•,•,•,•)
(1,•,•,•)
(2,•,•,•)
(3,•,•,•)
(4,•,•,•)
(1,2,•,•)
(1,3,•,•)
(1,3,4,2)

## Slide 42
*, *, *, *
1,*,*,*
1 [0, 4] L1=-4
3 [4, 5]
4 [5, 10] L4=0
3 [10, 15] L3=4
2 [15, 17] L2=5
2,*,*,*
2 [1, 3] L2=-9
1 [3, 7] L1=-1
4 [7, 12] L4=2
3 [12, 18] L3=7
1,2,*,*
1 [0, 4] L1=-4
2 [4, 6] L2=-6
4 [6, 11] L4=1
3 [11, 17] L3=6
1,3,*,*
1 [0, 4] L1=-4
3 [4, 10] L3=-1
4 [10, 15] L4=5
2 [15, 17] L3=5
Schedule: 1, 3, 4, 2,
4,*,*,*
either job 1 or 2 can be processed before 4 !
3,*,*,*
job 2 can be processed before 3 !

## Slide 43
Larger Example
Solve by branch-and-bound the scheduling problem 1 | rj | Lmax with the following job data:

## Slide 44
*, *, *, *, *, *, *
1, *, *, *, *, *, *
1 [0, 6] L1 = -2
2 [6, 14] 10 left
4 [14, 24] L4 = 0
2 [24, 34] L2 = -8
3 [34, 46] L3 = 2
6 [46, 50] 13 left
7 [50, 66] L7 = -2
6 [66, 79] L6 = -6
5 [79, 89] L5 = -1
Lower bound = 2
2, *, *, *, *, *, *
2 [0, 18] L2 = -24
1 [18, 24] L1 = 16 >2
3, *, *, *, *, *, *
3 [0, 12] L3 = -32
1 [12, 18] L1 = 10 >2
Solution…
jobs ordered by EDD: 1, 4, 2, 3, 7, 6, 5

## Slide 45
1, 2, *, *, *, *, *
1 [0, 6] L1 = -2
2 [6, 24] L2 = -18
4 [24, 34] L4 = 10
3 [34, 46] L3 = 2
6 [46, 50] 13 left
7 [50, 66] L7 = -2
6 [66, 79] L6 = -6
5 [79, 89] L5 = -1
Lower bound = 10
1, 4, *, *, *, *, *
1 [0, 6] L1 = -2
4 [14, 24] L4 = 0
2 [24, 42] L2 = 0
3 [42, 54] L3 = 10>4
...
1, 5, *, *, *, *, *
1 [0, 6] L1 = -2
5 [25, 35] L5 = -55
4 [35, 45] L4 = 21 > 4
...
1, 6, *, *, *, *, *
1 [0, 6] L1 = -2
6 [25, 42] L6 = -43
4 [42, 52] L4 = 28 > 4
...
1, 7, *, *, *, *, *
1 [0, 6] L1 = -2
7 [50, 66] L7 = -2
4 [66, 76] L4 = 53 > 4
...
1, *, *, *, *, *, *
1, 3, *, *, *, *, *
1 [0, 6] L1 = -2
3 [6, 18] L3 = -26
4 [18, 28] L4 = 4
2 [28, 46] L2 = 4
6 [46, 50] 13 left
7 [50, 66] L7 = -2
6 [66, 79] L6 = -6
5 [79, 89] L5 = -1
Lower bound = 4

## Slide 46
1, 3, 2, *, *, *, *
1 [0, 6] L1 = -2
3 [6, 18] L3 = -26
2 [18, 36] L2 = -6
4 [36, 46] L4 = 22
6 [46, 50] 13 left
the same as before:
7 [50, 66] L7 = -2
6 [66, 79] L6 = -6
5 [79, 89] L5 = -1
1, 3, *, *, *, *, *
1, 3, 4, *, *, *, *
1 [0, 6] L1 = -2
3 [6, 18] L3 = -26
4 [18, 28] L4 = 4
2 [28, 46] L2 = 4
6 [46, 50] 13 left
the same as before:
7 [50, 66] L7 = -2
6 [66, 79] L6 = -6
5 [79, 89] L5 = -1
Lower bound = 4
1, 3, 5, *, *, *, *
1 [0, 6] L1 = -2
3 [6, 18] L3 = -26
5 [25, 35] L5 = -55
4 [35, 45] L4 = 21 >4
1, 3, 6, *, *, *, *
1 [0, 6] L1 = -2
3 [6, 18] L3 = -26
6 [25, 42] L6 = -43
4 [42, 52] L4 = 28 >4
1, 3, 7, *, *, *, *
1 [0, 6] L1 = -2
3 [6, 18] L3 = -26
7 [50, 66] L5 = -2
4 [66, 76] L4 = 53 >4

## Slide 47
1, 3, 4, *, *, *, *
1, 3, 4, 2, *, *, *
1 [0, 6] L1 = -2
3 [6, 18] L3 = -26
4 [18, 28] L4 = 4
2 [28, 46] L2 = 4
6 [46, 50] 13 left
the same as before:
7 [50, 66] L7 = -2
6 [66, 79] L6 = -6
5 [79, 89] L5 = -1
Lower bound = 4
1, 3, 4, 5, *, *, *
1, 3, 4, 6, *, *, *
1, 3, 4, 7, *, *, *
Solution…

## Slide 48
1, 3, 4, 2, 5, *, *
1 [0, 6] L1 = -2
3 [6, 18] L3 = -26
4 [18, 28] L4 = 4
2 [28, 46] L2 = 4
5 [46, 56] L5 = -34
7 [56, 72] L7 = 4
6 [72, 89] L6 = 4
Lower bound = 4
1, 3, 4, 2, *, *, *
1, 3, 4, 2, 6, *, *
1, 3, 4, 2, 7, *, *
Schedule: 1, 3, 4, 2, 5, 7, 6
Lmax = 4
non-preemptive schedule is obtained!
Solution…

## Slide 49
*, *, *, *, *, *, *
1
1, 3, 4, 2, 5, 7
1, 3, 4, 2, 5, 7, 6
2
3
LB=2
1, 2
1, 7
1, 3, 2
1, 6
1, 5
1, 4
1, 3
1, 3, 7
1, 3, 6
1, 3, 5
1, 3, 4
1, 3, 4, 2
1, 3, 4, 2, 5
LB=4
LB=4
LB=4
LB=4
LB=4
Solution…

## Slide 50
Beam Search
Appendix C.4
Branch and Bound:
  Considers every node
  Guarantees optimum
  Usually too slow
Beam search
  Considers only most promising nodes
  (beam width)
  Does not guarantee convergence to optimal solution
  Much faster

## Slide 51
Single Machine Example (Total Weighted Tardiness)

## Slide 52
Branching (Beam width = 2)
(•,•,•,•)
(1,•,•,•)
(2,•,•,•)
(3,•,•,•)
(4,•,•,•)
(1,4,2,3)
(2,4,1,3)
(3,4,1,2)
(4,1,2,3)
ATC Rule
408
436
814
440
ATC Rule : Appendix C.3

## Slide 53
Beam Search
(•,•,•,•)
(1,•,•,•)
(2,•,•,•)
(3,•,•,•)
(4,•,•,•)
(1,2,•,•)
(1,3,•,•)
(1,4,•,•)
(2,1,•,•)
(2,3,•,•)
(2,4,•,•)
(2,4,3,1)
(2,4,1,3)
(1,4,3,2)
(1,4,2,3)

## Slide 54: Discussion
Implementation tradeoff:
  Careful evaluation of nodes (accuracy)
  Crude evaluation of nodes (speed)
Two-stage procedure
  Filtering
    crude, but fast, evaluation
    filter width = set of nodes having the most promise
    filter width > beam width
  Careful evaluation of remaining nodes in the “beam”

## Slide 55: Total Weighted Tardiness
Problem:
No efficient algorithm (NP-Hard)
Branch and bound can only solve small problems (<100 jobs)
Are there any special cases we can solve?

## Slide 56: Case 1: Tight Deadlines
Assume dj=0
Then
We know that WSPT is optimal for this problem!
The WSPT is optimal in the extreme case and should be a good heuristic whenever due dates are tight

## Slide 57: Case 2: “Easy” Deadlines
Theorem: If the deadlines are sufficiently spread out then the Minimum Slack (MS) rule
is optimal (proof a bit harder)
Conclusion: The MS rule should be a good heuristic whenever deadlines are widely spread out

## Slide 58: Apparent Tardiness Cost (ATC) Dispatching Rule
Two good heuristics
  Weighted Shortest Processing Time (WSPT )
    optimal with due dates zero
  Minimum Slack (MS)
    Near optimal when due dates are “spread out”
  Any real problem is somewhere in between
ATC combines the characteristics of these rules into one composite dispatching rule
ATC Rule : Appendix C.3

## Slide 59: Apparent Tardiness Cost (ATC) Dispatching Rule
Dynamic ranking index
When machine becomes free:
  Compute index for all remaining jobs that are currently waiting
  Select job with highest value
Scaling constant
average pj of the remaining jobs (rounded down)

## Slide 60: Special Cases
If K is very large:
  ATC reduces to WSPT
If K is very small and no overdue jobs:
  ATC reduces to MS
If K is very small and many overdue jobs:
  ATC reduces to WSPT applied to overdue jobs
Apparent Tardiness Cost (ATC) Dispatching Rule

## Slide 61: Choosing K
Value of K determined empirically
Related to the due date tightness factor
and the due date range factor
Apparent Tardiness Cost (ATC) Dispatching Rule

## Slide 62: Apparent Tardiness Cost (ATC) Dispatching Rule
Usually 1.5  K  4.5
Rules of thumb:
  Fix K=2 for single machine or flow shop.
  Fix K=3 for dynamic job shops.
Adjusted to reduce weighted tardiness cost in extremely slack or congested job shops
Statistical analysis/empirical experience

## Slide 63
Total Weighted Tardiness

## Slide 64
Total Weighted Tardiness

## Slide 65
Total Weighted Tardiness

## Slide 66
If for two jobs j and k,
and
then there exists an optimal solution in which j appears before k
Total Weighted Tardiness

## Slide 67
Total Weighted Tardiness

## Slide 68
Total Weighted Tardiness
Jobs | 1 | 2 | 3 | 4
wj | 4 | 5 | 3 | 5
pj | 12 | 8 | 15 | 9
dj | 16 | 26 | 25 | 27

## Slide 69: Total Earliness and Tardiness
definition: Earliness of job i = Ei = max { di-Ci , 0 }
Objective is to minimize total Earliness and Tardiness
Not a regular measure of performance
  if Ci decreases, earliness could increase
  leads to the possibility of deliberately inserting idle time
  minimizing earliness tends to minimize work-in-process inventory, a core objective in Just-in-Time production scheduling

## Slide 70: Total Earliness and Tardiness Common Due Date
all di = d
no inserted idle time
  once processing begins, jobs continually scheduled
Two sets of jobs can be defined:
  J1 : all jobs with completion times ≤ d
  J2 : all jobs with completion times > d
Optimal sequencing rule:
  Sequence J1 using WLPT
  Sequence J2 using WSPT

## Slide 71: Total Earliness and Tardiness Common “Loose” Due Date
If d is large enough such that no job begins at t = 0,
  an optimal schedule exists with a job i with Ci = d
If all earliness and tardiness penalties = 1,
  order all jobs using LPT
  assign first job from list to J1, next job to J2, and alternate thereafter until all jobs have been assigned
  J1 already in LPT order; reverse the order of jobs in J2 to achieve SPT ordering
Example (with all weights = 1):
job i | 1 | 2 | 3 | 4 | 5
pi | 5 | 7 | 4 | 8 | 12
LPT order | 4 | 3 | 5 | 2 | 1
k:Jk | 2 | 1 | 1 | 2 | 1
LPT ordered J1 : 5-2-3
SPT ordered J2 : 1-4

## Slide 72: Total Earliness and Tardiness Common “Loose” Due Date
Job b in the optimal sequence is completed at the due date where b is the smallest integer satisfying
Example:
d = 50
job i | 1 | 2 | 3 | 4 | 5
pi | 5 | 7 | 4 | 8 | 12
wi’ | 4 | 8 | 8 | 12 | 15
wi’’ | 7 | 7 | 4 | 20 | 15
order by non-increasing wi’+ wi’’
  4,5,2,3,1
WLPT J1 : 5-4
WSPT J2 : 1-2-3 or 1-3-2
b | 1 | 2
J1 sum(1,b) | 32 | 62

## Slide 73: Total Earliness and Tardiness Common “Tight” Due Date
“tight” due date implies a job must begin at t = 0
  an optimal sequence no longer has a job completing at t = d and no optimal rule-based procedure exists
Heuristic procedure for constructing sequence (no earliness or tardiness penalties)
0. LPT order jobs
  set t1d , t2Σ(pj)-d , k1
  if t1>t2 then assign job to earliest available slot t1 t1-pk
  else assign job to latest available slot t2 t2-pk
  if k<n then kk+1 , go to (2)
  else STOP

## Slide 74: Total Earliness and Tardiness Common “Tight” Due Date
Example: d = 15
job i | 1 | 2 | 3 | 4 | 5
pi | 5 | 7 | 4 | 8 | 12
LPT order k | 4 | 3 | 5 | 2 | 1
k | t1 | t2 | assignment | partial seq.
1 | 15 | 36-15=21 | 15<21job 5 pushed late | {*,*,*,*,5}
2 | 15 | 21-12=9 | 15>9job 4 pushed early | {4,*,*,*,5}
3 | 15-8=7 | 9 | 7<9job 2 pushed late | {4,*,*,2,5}
4 | 7 | 9-7=2 | 7>2job 1 pushed early | {4,1,*,2,5}
5 |  |  |  | {4,1,3,2,5}

## Slide 75: Total Earliness and Tardiness Distinct Due Dates
Common due date properties do not apply (NP-hard)
May need to insert idle time to further minimize objective
Two-stage scheduling heuristic
  Build a sequence
  Determine start times for jobs in the sequence
Property: If dj+1- dj ≤ pj+1  no idle time between j and j+1
A cluster of jobs [u,v] is a series of jobs starting with j = u-1 and ending with j = v-1 for which the no idle time property holds
Idle time insertion algorithm starts with a sequence with no idle time
Algorithm determines the optimal shift of each cluster to minimize E/L objective for a given sequence

## Slide 76
Local (Neighborhood) Search
Step. 1. Initialisation
k=0
Select a starting solution S0S
Record the current best-known solution by setting Sbest = S0 and best_cost = F(Sbest)
Step 2. Choice and Update
Choose a Solution Sk+1N(Sk) If the choice criteria cannot be satisfied by any member of N(Sk), then the algorithm stops
if F(Sk+1) < best_cost then Sbest = Sk+1 and best_cost = F(Sk+1)
Step 3. Termination
If termination conditions apply
then the algorithm stops
else k = k+1 and go to Step 2.

## Slide 77
Global Optimum: better than all other solutions
Local Optimum: better than all solutions in a certain neighborhood
Local (Neighborhood) Search

## Slide 78: Neighborhood Search
Seeks local (myopic) optimal solution
Initial n job seed sequence:
  at random
  solution of appropriate heuristic
Generate solutions in neighborhood of seed
  API: n-1 API’s describe neighborhood
  TPUF: “top priority up front”
    TPUF neighborhood for seed 1-2-3-4 :
      2-1-3-4
      3-1-2-4
      4-1-2-3

## Slide 79: Neighborhood Search
  PI: General pairwise interchange
    all (n)(n-1)/2 possible sequences generated
    PI neighborhood for seed 1-2-3-4 :
      2-1-3-4
      3-2-1-4
      4-2-3-1
      1-3-2-4
      1-4-3-2
      1-2-4-3
  K-move: move K jobs to left (or right) at once
    (2K-1)n sequences generated
    about as accurate as PI with 2K/n the computational cost
    TPUF is K-move with K=1

## Slide 80: Neighborhood Search
  k-way interchange
    interchange among every possible subset of k jobs
    n!/(k!(n-k)!) sequences
    n-way is complete enumeration
    k>3 becomes too costly to be practical
Selecting next seed
  evaluate all solutions in neighborhood and choose best
  choose first improved solution… usually more efficient
Terminating neighborhood search
  no (or small) improvement over neighborhood
  no (or small) improvement over expanded neighborhood
    after having gone from API to PI, for example

## Slide 81: Adjacent Pairwise Interchange (API)
Minimize Total Tardiness
Use EDD rule to provide “seed” sequence to minimize total tardiness
Examine API neighborhood of seed
First improved sequence becomes the next seed
Example: (min total tardiness = 755)
Job i | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
pi | 121 | 147 | 102 | 79 | 130 | 83 | 96 | 88
di | 260 | 269 | 400 | 266 | 337 | 336 | 683 | 719

## Slide 82: Adjacent Pairwise Interchange (API)
Calculating total tardiness for API generated sequences
S | Ti | S | Ti | S | Ti | S | Ti | S | Ti | S | Ti | S | Ti | S | Ti
1 | 0 | 4 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
4 | 0 | 1 | 0 | 2 | 0 | 4 | 0 | 4 | 0 | 4 | 0 | 4 | 0 | 4 | 0
2 | 78 | 2 | 78 | 4 | 81 | 6 | 0 | 2 | 78 | 2 | 78 | 2 | 78 | 2 | 78
6 | 94 | 6 | 94 | 6 | 94 | 2 | 161 | 5 | 140 | 6 | 94 | 6 | 94 | 6 | 94
5 | 223 | 5 | 223 | 5 | 223 | 5 | 223 | 6 | 224 | 3 | 132 | 5 | 223 | 3 | 223
3 | 262 | 3 | 262 | 3 | 262 | 3 | 262 | 3 | 262 | 5 | 325 | 7 | 0 | 5 | 262
7 | 75 | 7 | 75 | 7 | 75 | 7 | 75 | 7 | 75 | 7 | 75 | 3 | 358 | 8 | 31
8 | 127 | 8 | 127 | 8 | 127 | 8 | 127 | 8 | 127 | 8 | 127 | 8 | 127 | 7 | 163
Σ T | 859 |  | 859 |  | 862 |  | 848 |  | 906 |  | 831 |  | 880 |  | 851

## Slide 83: Adjacent Pairwise Interchange (API)
First improved sequence is seed for another API iteration
 |  |  |  |  |  |  |  | Σ T
1 | 4 | 6 | 2 | 5 | 3 | 7 | 8 | 848
4 | 1 | 6 | 2 | 5 | 3 | 7 | 8 | 848
1 | 6 | 4 | 2 | 5 | 3 | 7 | 8 | 865
1 | 4 | 2 | 6 | 5 | 3 | 7 | 8 | 781

## Slide 84: Adjacent Pairwise Interchange (API)
Another total tardiness example…
Job i | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
pi | 138 | 132 | 153 | 89 | 141 | 131 | 107 | 103
di | 466 | 459 | 402 | 422 | 478 | 392 | 368 | 385
 |  |  |  |  |  |  |  | Σ T
7 | 8 | 6 | 3 | 4 | 2 | 1 | 5 | 1412
8 | 7 | 6 | 3 | 4 | 2 | 1 | 5 | 1412
7 | 6 | 8 | 3 | 4 | 2 | 1 | 5 | 1412
7 | 8 | 3 | 6 | 4 | 2 | 1 | 5 | 1422
7 | 8 | 6 | 4 | 3 | 2 | 1 | 5 | 1348
EDD Seq

## Slide 85: Adjacent Pairwise Interchange (API)
 |  |  |  |  |  |  |  | Σ T
7 | 8 | 6 | 4 | 3 | 2 | 1 | 5 | 1348
8 | 7 | 6 | 4 | 3 | 2 | 1 | 5 | 1348
7 | 6 | 8 | 4 | 3 | 2 | 1 | 5 | 1348
7 | 8 | 4 | 6 | 3 | 2 | 1 | 5 | 1378
7 | 8 | 6 | 3 | 4 | 2 | 1 | 5 | 1412
7 | 8 | 6 | 4 | 2 | 3 | 1 | 5 | 1327
new seed seq
min Σ T = 1300

## Slide 86: Neighborhood Search Example
Investigating neighborhood search strategies to minimize total tardiness
Seed generated using Longest Processing Time first rule (LPT)… iteration 1
Job i | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
pi | 138 | 132 | 153 | 89 | 141 | 131 | 107 | 103
di | 466 | 459 | 402 | 422 | 478 | 392 | 368 | 385
Seq | 3 | 5 | 1 | 2 | 6 | 7 | 8 | 4 | 
Ci | 153 | 294 | 432 | 564 | 695 | 802 | 905 | 994 | Σ Ti
Ti | 0 | 0 | 0 | 105 | 303 | 434 | 520 | 572 | 1934

## Slide 87: Neighborhood Search Example
API… iteration 2
API… iteration 3
Seq | 3 | 5 | 1 | 2 | 7 | 6 | 8 | 4 | 
Ci | 153 | 294 | 432 | 564 | 671 | 802 | 905 | 994 | Σ Ti
Ti | 0 | 0 | 0 | 105 | 303 | 410 | 520 | 572 | 1910
Seq | 3 | 5 | 1 | 2 | 7 | 8 | 6 | 4 | 
Ci | 153 | 294 | 432 | 564 | 671 | 774 | 905 | 994 | Σ Ti
Ti | 0 | 0 | 0 | 105 | 303 | 389 | 513 | 572 | 1882

## Slide 88: Neighborhood Search Example
API… iteration 8
API… iteration 20
min total tardiness = 1300
Seq | 3 | 7 | 8 | 4 | 6 | 2 | 1 | 5 | 
Ci | 153 | 260 | 363 | 452 | 583 | 715 | 853 | 994 | Σ Ti
Ti | 0 | 0 | 0 | 30 | 191 | 256 | 387 | 516 | 1380
Seq | 3 | 7 | 5 | 1 | 8 | 2 | 4 | 6 | 
Ci | 153 | 260 | 401 | 539 | 642 | 774 | 863 | 994 | Σ Ti
Ti | 0 | 0 | 0 | 73 | 257 | 315 | 441 | 602 | 1688

## Slide 89: Neighborhood Search Example
Using PI with same LPT seed at iteration 1
  iteration 2:
PI… iteration 6
Seq | 3 | 4 | 1 | 2 | 6 | 7 | 8 | 5 | 
Ci | 153 | 242 | 380 | 512 | 643 | 750 | 853 | 994 | Σ Ti
Ti | 0 | 0 | 0 | 53 | 251 | 382 | 468 | 516 | 1670
Seq | 7 | 6 | 8 | 4 | 2 | 3 | 1 | 5 | 
Ci | 107 | 238 | 341 | 430 | 562 | 715 | 853 | 994 | Σ Ti
Ti | 0 | 0 | 0 | 8 | 103 | 313 | 387 | 516 | 1327

## Slide 90: Neighborhood Search Example
PI… iteration 9
  Optimal Solution
More Sophisticated Neighborhood Search Approaches:
  Simulated Annealing (App. C.5)
  Tabu Search (App. C.5
  Genetic Algorithms (App. C.6)
Seq | 7 | 6 | 8 | 4 | 2 | 1 | 5 | 3 | 
Ci | 107 | 238 | 341 | 430 | 562 | 700 | 841 | 994 | Σ Ti
Ti | 0 | 0 | 0 | 8 | 103 | 234 | 363 | 592 | 1300

## Slide 91: Construction versus Improvement Heuristics
Construction Heuristics
  Start without a schedule
  Add one job at a time
  Dispatching rules and beam search
Improvement Heuristics
  Start with a schedule
  Try to find a better ‘similar’ schedule
Can be combined

## Slide 92: Backward-Forward Heuristic (BF)
D.R. Sule, Industrial Scheduling, PWS Publishing Co., Boston, 1997.
Backward phase : construct an initial sequence, starting with the last position in the sequence.
Forward phase : attempt to improve the solution by moving later jobs in the sequence forward to earlier positions.
Backward phase notation:
  N = number of jobs
  S = set of sequenced jobs
  Sc = set of unsequenced jobs
  pi = processing time for job i
  di = due date for job i
  wi” = tardiness penalty for job i

## Slide 93: Backward-Forward Heuristic (BF)
Backward phase algorithm:
FOR n = N, N-1, N-2,…, 1
SET
Pi = tardiness penalty for unsequenced job i
= max{(t-di)wi’’ , 0}
FIND i* = job to sequence in position n
= …largest pi is tie-breaker
Sc = Sc / {i*}
ENDFOR
OUTPUT: S

## Slide 94: Backward-Forward Heuristic (BF)
Backward phase example:
Iterations of algorithm:
job i | 1 | 2 | 3 | 4
pi | 2 | 4 | 3 | 1
di | 1 | 2 | 4 | 6
wi’’ | 1 | 1 | 1 | 1
n | Sc | t | Pi , iεSc | i*
4 | 1,2,3,4 | 10 | 9,8,6,4 | 4
3 | 1,2,3 | 9 | 8,7,5 | 3
2 | 1,2 | 6 | 5,4 | 2
1 | 1 | 2 | 1 | 1
S=1-2-3-4
P(S)=
= 14

## Slide 95: Backward-Forward Heuristic (BF)
Forward phase
  k = “lag” between job positions in S
  J[i] = job in position i in sequence
  Algorithm:
  (1) SET k = N-1
  (2) SET j = k+1
  (3) SWAP J[j] and J[j-k] to form S’
  FIND P(S’)
  IF P(S’)>P(S), SET j  j+1
  IF j  N, go to (3)
  ELSE, go to (4)
  ELSE, IF SWAP not done earlier, then S  S’ , go to (1)
  ELSE, SET j  j+1
  IF j < N, go to (3)
  ELSE,
  (4) k  k-1
  IF k > 0, go to (2)
  ELSE, STOP (with S)

## Slide 96: Backward-Forward Heuristic (BF)
Example continued with forward phase algorithm
lag k | [j] | [j-k] | S’ | C[i]-d[i] | P(S’)
3 | 4 | 1 | 4-2-3-1 | 1-6, 5-2, 8-4, 10-1 | 16 > P(S)
2 | 3 | 1 | 3-2-1-4 | 3-4, 7-2, 9-1, 10-6 | 17 > P(S)
2 | 4 | 2 | 1-4-3-2 | 2-1, 3-6, 6-4, 10-2 | 11 < P(S)
S = 1-4-3-2

## Slide 97: Backward-Forward Heuristic (BF)
Continuing the forward algorithm on S = 1-4-3-2
lag k | [j] | [j-k] | S’ | C[i]-d[i] | P(S’)
3 | 4 | 1 | 2-4-3-1 | 4-2, 5-6, 8-4, 10-1 | 15>P(S)=11
2 | 3 | 1 | 3-4-1-2 | 3-4, 4-6, 6-1, 10-2 | 13 > P(S)
2 | 4 | 2 | 1-2-3-4 | done earlier… | 14 > P(S)
1 | 2 | 1 | 4-1-3-2 | 1-6, 3-1, 6-4, 10-2 | 12 > P(S)
1 | 3 | 2 | 1-3-4-2 | 2-1, 5-4, 6-6, 10-2 | 10 < P(S)
S = 1-3-4-2

## Slide 98: Backward-Forward Heuristic (BF)
Continuing the forward algorithm on S = 1-3-4-2
lag k | [j] | [j-k] | S’ | C[i]-d[i] | P(S’)
3 | 4 | 1 | 2-3-4-1 | 4-2, 7-4, 8-6, 10-1 | 16>P(S)=10
2 | 3 | 1 | 4-3-1-2 | 1-6, 4-4, 6-1, 10-2 | 13 >P(S)
2 | 4 | 2 | 1-2-4-3 | 2-1, 6-2, 7-6, 10-4 | 12 > P(S)
1 | 2 | 1 | 3-1-4-2 | 3-4, 5-1, 6-6, 10-2 | 12 > P(S)
1 | 3 | 2 | 1-4-3-2 | done earlier | 11 > P(S)
1 | 4 | 3 | 1-3-2-4 | 2-1, 5-4, 9-2, 10-6 | 13 > P(S)
S* = 1-3-4-2 P(S*) = 10

## Slide 99: Backward-Forward Heuristic (BF)
Total Earliness and Tardiness Objective
  wi’ = earliness penalty rate for completing job i before di
  BF algorithm adjustment in backward phase:
  Pi = max { (t-di)wi’’ , (di-t)wi’ }
Early and Late due dates
  DEi : early penalty applies if Ci < DEi
  DLi : late penalty applies if Ci > DLi
  Backward phase adjustment:
  Pi = max {(DEi-Ci)wi’ , 0 , (Ci-DLi)wi’’ }
    if several jobs have lowest Pi , use job with longest pi

## Slide 100: Parallel Machine Model Characteristics
Identical machines in parallel Pm
m machines in parallel
Job j requires a single operation and may be processed on any of the m machines
If job j may be processed on any one machine belonging to a given subset Mj Pm | Mj | ...
Machines in parallel with different speeds Qm
Unrelated machines in parallel Rm
machines have different speeds for different jobs

## Slide 101: Parallel Machine Models
Resource allocation in addition to sequencing
  Single stage
  Identical processors assumed (initially…)
  Independent jobs (initially…)
  Job processed on one machine at a time (initially…)
Pm l l Cmax : Makespan objective without preemption
  “load balancing” objective
  Integer Program:
    xij = 1, if job i assigned to machine j
      = 0, if not

## Slide 102: Throughput and Makespan
Throughput
  Defined by bottleneck machines
Makespan
Minimizing makespan tends to
  maximize throughput and
  balance load

## Slide 103: Parallel Machine Models Makespan Pm l l Cmax
Largest Processing Time heuristic LPT
  Sequence jobs with LPT rule
  In order, assign jobs to machines least loaded
    shortest jobs used near end to refine balance among machines
LPT worst case analysis:
Worst case analysis of random selection from a list

## Slide 104: Parallel Machine Models Makespan Pm l l Cmax
LPT example:
  LPT order: 2-5-3-1-4
  Cmax = 24
job i | 1 | 2 | 3 | 4 | 5
pi | 7 | 24 | 14 | 6 | 18
t | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
m1 |  |  |  |  |  |  |  |  |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
m2 |  |  |  |  |  |  |  |  | 5 |  |  |  |  |  |  |  |  |  |  |  |  | 4 |  |  | 
m3 |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  | 

## Slide 105: Parallel Machine Models Makespan Pm l l Cmax
MULTIFIT heuristic
Reference: E.G. Coffman, M.R. Garey, D.S. Johnson (1978) “An Application of Bin-Packing to Multiprocessor Scheduling”, SIAM Journal on Computing, Vol. 7, pp. 1-17
  better worst case bound (k = # of iterations)
  Define:
  CL and CU adjusted by algorithm
  Estimate of Cmax = final value of CU

## Slide 106: Parallel Machine Models Makespan Pm l l Cmax
MULTIFIT Algorithm:
  0. SET I  0, LPT order the jobs.
  SET C  (1/2)(CL + CU)
  I  I + 1
  Assign the jobs in succession to the lowest indexed machine that can complete the job within the capacity, C
    First Fit Decreasing (FFD) bin packing heuristic
  If all the jobs can be assigned to the m machines, then SET CU  C and go to step 4.
  Else, SET CL  C and go to step 4.
  If I = k (prespecified), STOP
  Else, go to step 1.

## Slide 107: Parallel Machine Models Makespan Pm l l Cmax
MULTIFIT example: m = 3
  CU = max { 24, 2(69)/3 } = 46
  CL = max { 24, 69/3 } =24
  SET I = 0
job i | 1 | 2 | 3 | 4 | 5
pi | 7 | 24 | 14 | 6 | 18
LPT job sort | 2 | 5 | 3 | 1 | 4
sorted pi | 24 | 18 | 14 | 7 | 6

## Slide 108: Parallel Machine Models Makespan Pm l l Cmax
step 1: SET C = ½[24+46] = 35 , I = 1
step 2:
step 3: CU = C = 35
LPT job i | 1 | 2 | 3 | 4 | 5
i  mK | 1 | 2 | 2 | 1 | 3
m1 | 11 | 11 | 11 | 4 | 4
m2 | 35 | 17 | 3 | 3 | 3
m3 | 35 | 35 | 35 | 35 | 29
remaining capacity
on mK
job i | 1 | 2 | 3 | 4 | 5
pi | 7 | 24 | 14 | 6 | 18
LPT job sort | 2 | 5 | 3 | 1 | 4
sorted pi | 24 | 18 | 14 | 7 | 6

## Slide 109
step 1: SET C = ½[24+35] = 29.5 , I = 2
step 2:
step 3: CU = C = 29.5
Parallel Machine Models Makespan Pm l l Cmax
LPT job i | 1 | 2 | 3 | 4 | 5
i  mK | 1 | 2 | 3 | 2 | 3
m1 | 5.5 | 5.5 | 5.5 | 5.5 | 5.5
m2 | 29.5 | 11.5 | 11.5 | 4.5 | 4.5
m3 | 29.5 | 29.5 | 15.5 | 15.5 | 9.5
remaining capacity
on mK
job i | 1 | 2 | 3 | 4 | 5
pi | 7 | 24 | 14 | 6 | 18
LPT job sort | 2 | 5 | 3 | 1 | 4
sorted pi | 24 | 18 | 14 | 7 | 6

## Slide 110
step 1: SET C = ½[24+29.5] = 26.75 , I = 3
step 2:
step 3: CU = C = 26.75
Parallel Machine Models Makespan Pm l l Cmax
LPT job i | 1 | 2 | 3 | 4 | 5
i  mK | 1 | 2 | 3 | 2 | 3
m1 | 2.75 | 2.75 | 2.75 | 2.75 | 2.75
m2 | 26.75 | 8.75 | 8.75 | 1.75 | 1.75
m3 | 26.75 | 26.75 | 12.75 | 12.75 | 6.75
remaining capacity
on mK
job i | 1 | 2 | 3 | 4 | 5
pi | 7 | 24 | 14 | 6 | 18
LPT job sort | 2 | 5 | 3 | 1 | 4
sorted pi | 24 | 18 | 14 | 7 | 6

## Slide 111
step 1: SET C = ½[24+26.75] = 25.375 , I = 4
step 2:
step 3: CU = C = 25.375
Parallel Machine Models Makespan Pm l l Cmax
LPT job i | 1 | 2 | 3 | 4 | 5
i  mK | 1 | 2 | 3 | 2 | 3
m1 | 1.375 | 1.375 | 1.375 | 1.375 | 1.375
m2 | 25.375 | 7.375 | 7.375 | .375 | .375
m3 | 25.375 | 25.375 | 11.375 | 11.375 | 5.375
remaining capacity
on mK
job i | 1 | 2 | 3 | 4 | 5
pi | 7 | 24 | 14 | 6 | 18
LPT job sort | 2 | 5 | 3 | 1 | 4
sorted pi | 24 | 18 | 14 | 7 | 6

## Slide 112
step 1: SET C = ½[24+25.375] = 24.69 , I = 5
step 2:
step 3: CU = C = 24.69
Same schedule produced for I > 5 (same as LPT produces)
Parallel Machine Models Makespan Pm l l Cmax
LPT job i | 1 | 2 | 3 | 4 | 5
i  mK | 1 | 2 | 3 | 3 | 2
m1 | .69 | .69 | .69 | .69 | .69
m2 | 24.69 | 6.69 | 6.69 | 6.69 | .69
m3 | 24.69 | 24.69 | 10.69 | 3.69 | 3.69
remaining capacity
on mK

## Slide 113
If the number of parallel machines at least as large as the the number of jobs  classic Project Scheduling problem
Algorithmic approach used to minimize makespan of a project is the Critical Path Method
Forward procedure:
  Starting at time zero, calculate the earliest each job can be started
  The completion time of the last job is the makespan
Backward procedure
  Starting at time equal to the makespan, calculate the latest each job can be started so that this makespan is realized
Parallel Machine Models Makespan Pm l prec l Cmax
A
B
E
D
C

## Slide 114
“Harder” class of parallel machine scheduling problems have 1 < m < n
Easy special case: Pm l pj=1 , tree l Cmax
Trees:
    Intree Outtree
Parallel Machine Models Makespan Pm l prec l Cmax
L1
L2
L3
L1
L2
L3
root node
root node

## Slide 115
Critical Path Rule (CP) :
  highest priority to job in front of longest “string” (jobs on highest level first)
  ties arbitrarily broken
  optimal scheduling rule for intrees and outtrees with unit processing times
CP rule used as a heuristic for arbitrary precedence constraints and all processing times equal
  worst case bound for m=2: (even worse for m>2…)
Parallel Machine Models Makespan Pm l prec l Cmax

## Slide 116
Largest Number of Successors first : (LNS)
  heuristic for arbitrary precedence and equal processing times
  optimal for intrees and outtrees (since equivalent to CP, in that case)
  Example: nodes labeled with number of successor nodes
Parallel Machine Models Makespan Pm l prec l Cmax
13
5
8
6
4
6
4
4
3
3
2
1
0
1

## Slide 117
Applying the LNS rule for arbitrary precedence and arbitrary processing times
  Assign to each terminal job a label equal to its processing time
  Assign to job j the label βj ,where
  S(j) is the set of all jobs on all paths in the precedence diagram that succeed job j
  Assign the job with no unscheduled predecessors with the largest label to the least loaded machine
Parallel Machine Models Makespan Pm l prec l Cmax

## Slide 118
Parallel Machine Models Critical Path Method Example / LNS labeling
1
2
3
6
9
5
8
4
7
11
10
12
14
13
113
50
44
32
71
55
50
37
33
27
12
22
13
5

## Slide 119
Machine loading using LNS labels (m = 3):
Parallel Machine Models Makespan Pm l prec l Cmax
t |  | 5 |  | 11 | 14 |  |  | 23 | 26 |  | 32 | 33 | 36 |  | 42 | 43 | 50 | 51 | 56 |  | 
m1 | 1 |  |  |  |  | 5 |  |  |  |  | 8 |  |  |  |  |  |  |  |  |  | 
m2 |  |  | 3 |  |  | 6 |  |  |  |  | 9 |  |  |  | 11 |  | 12 |  | 14 |  | 
m3 |  |  | 2 |  | 4 |  |  |  | 7 |  |  |  | 10 |  |  |  | 13 |  |  |  | 

## Slide 120
Preemption: processing of job may be interrupted by beginning to process another job
  preempt-repeat: preempted job must start over
  preempt-resume: preempted job resumes processing where it was interrupted (our assumption here…)
LP formulation of Pm l prmp l Cmax
  let xij = amount of processing time for job j on machine i
Parallel Machine Models Makespan Pm l prmp l Cmax

## Slide 121
Lower bound on Cmax
Pm l prmp l Cmax Algorithm
  Load all jobs in LPT order on a single machine
  From the beginning of the single machine schedule, allocate C*max “chunks” to each machine in turn with any residual chunk < C*max allocated to the last machine
  Note: Since Cmax= C*max , schedule is optimal
Parallel Machine Models Makespan Pm l prmp l Cmax

## Slide 122
Pm l prmp l Cmax Algorithm Example
  C*max = max { 20, 65/3 } = 21.67
Parallel Machine Models Makespan Pm l prmp l Cmax
job i | 1 | 2 | 3 | 4 | 5
pi | 7 | 20 | 14 | 6 | 18
LPT job sort | 2 | 5 | 3 | 1 | 4
sorted pi | 20 | 18 | 14 | 7 | 6
t | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 8.67 |  |  |  | 13 | 14 | 15.67 | 16.33 |  |  |  | 20 |  | 21.67
m1 |  |  |  |  |  |  |  |  | 2 |  | 2 |  |  |  |  |  |  |  |  |  |  | 5
m2 |  |  |  |  |  |  |  |  | 5 |  |  |  |  |  |  |  |  |  |  | 3 |  | 
m3 |  |  |  |  |  |  | 3 |  |  |  |  | 1 |  |  |  |  |  | 4 |  |  |  | 

## Slide 123
SPT rule optimal for Pm l l ΣCj
Visualizing min ΣCj on a single machine
  min ΣCj =np[1] + (n-1)p[2] + … + p[n]
  for n = 3:
  shaded area is smallest when smallest pj matched with largest coefficient
Parallel Machine Models Total Completion Time Pm l l ΣCj
p[1] |  | 
p[1] | p[2] | 
p[1] | p[2] | p[3]
Number of jobs to do, n
C[3]
C[2]
C[1]

## Slide 124
Generalizing to m parallel machines:
  let i[j] = j-th job in sequence on machine i
  match m “1” coefficients with largest m pj’s
  match m “2” coefficients with next largest m pj’s , etc…
Dispatching implementation:
  place jobs in SPT order
  assign next job on list to least loaded machine (or in rotation) until all jobs are scheduled
  easily extended to dynamic case
Parallel Machine Models Total Completion Time Pm l l ΣCj

## Slide 125
WSPT is not optimal for Pm l l ΣwjCj
  but provides a very effective heuristic
WSPT dispatching implementation:
  place jobs in WSPT order ---> p[1]/w[1] < p[2]/w[2] < …
  assign next job on list to least loaded machine until all jobs are scheduled
WSPT Worst case bound on optimality for Pm l l ΣwjCj
Parallel Machine Models Total Weighted Completion Time Pm l l ΣwjCj

## Slide 126
WSPT Example:
  m=2
  Data:
  WSPT ordering: 5-6-2-1-4-3
Parallel Machine Models Total Weighted Completion Time Pm l l ΣwjCj
job j | 1 | 2 | 3 | 4 | 5 | 6
pj | 3 | 7 | 20 | 12 | 5 | 10
wj | 1 | 3 | 4 | 4 | 3 | 5
pj / wj | 3 | 2.33 | 5 | 3 | 1.67 | 2
t | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | … | 33
m1 |  |  | 5 |  |  |  |  |  | 2 |  |  |  |  |  |  |  |  | 4 |  |  |  |  |  |  | … | 
m2 |  |  |  |  |  | 6 |  |  |  |  |  | 1 |  |  |  |  |  |  | 3 |  |  |  |  |  | … | 

## Slide 127
Precedence Constraints: Pm l prec l ΣCj
  Critical Path (CP) rule provides optimal schedule for
  Pm l pj=1, outtree l ΣCj
  CP rule not optimal for intrees…
  CP rule: highest priority to job in front of longest “string” of jobs
Machine Restrictions: Pm l pj=1, Mj l ΣCj
  Least Flexible Job (LFJ) rule provides optimal schedule if Mj nested
  Among the available jobs when a machine becomes free, pick the job that can be processed on the smallest number of machines
  LFJ provides heuristic if Mj not nested
Parallel Machine Models Total Completion Time Pm l l ΣCj

## Slide 128
Rm : processing times of jobs are machine dependent with no systematic pattern
Integer Programming formulation:
  let xikj=1, if job j in position k on machine i
  =0, otherwise
Parallel Machine Models Total Completion Time, Unrelated Machines Rm l l ΣCj
each job put in 1 position
each position has 0 or 1 jobs assigned to it

## Slide 129
Integer Programming formulation:
  a weighted bipartite matching problem
  coefficient structure in the constraints guarantees a 0-1 solution
  thus, xikj integer restriction replaced by nonnegativity constraint
  thus, solved as a linear program
  inserted idle time possible in the solution
Parallel Machine Models Total Completion Time, Unrelated Machines Rm l l ΣCj

## Slide 130
A heuristic approach for Pm l l Σ Tj
  Reference: Dogramaci & Surkis (1979), “Evaluation of a Heuristic for Scheduling Independent Jobs on Parallel Identical Processors”, Management Science, Vol. 25, #12
  form priority list of n jobs
  assign next job from list to least loaded machine
  solve the 1 | | Σ Tj problem
  repeat steps (1), (2), and (3) for priority rules SPT, EDD, MS and choose the best schedule generated
Parallel Machine Models Due Date-related Issues