## Slide 1: Economic Lot Scheduling Problem
IE 419

## Slide 2: Economic Lot Scheduling Single Item, Single Machine
Continuous manufacturing, make-to-stock:
Domain:
  large number of identical jobs
  setup time/cost significant
  setup may be sequence dependent
  Longer planning horizon
  Long runs, large setup times: cost minimization
  Usually repetitive structure: rotation schedule
Degrees of freedom: cycle length, sequencing within cycle
Intuition: increasing lot size 
  inventory costs per unit of time 
  setup costs per unit of time 

## Slide 3
Standard ELSP:
1 machine: produces item j with rate Qj per time unit.
n items with processing time pj  Qj=1/pj
constant demand rate Dj
inventory costs hj, setup cost cjk (j  k), setup time sjk
cycle: j1, …,jh, corresponding run times: tj1, …,tjh
Economic Lot Scheduling Single Item, Single Machine
Notes: De grote formules hoeven niet geleerd te worden. De symbolen moeten wel bekend zijn, en met deze moet je een gegeven formule kunnen interpreteren. De interpretatie is dus wel belangrijk!

## Slide 4: Minimize Cost
Let x denote the cycle time
Demand over a cycle = Dx
Length of production run needed = Dx/Q = t
Inventory
Time
x
Economic Lot Scheduling Single Item, Single Machine
average inventory

## Slide 5
Setup cost rate = c/x
Average inventory holding cost
Total cost
Per item holding cost
Setup cost per run
Economic Lot Scheduling Single Item, Single Machine

## Slide 6: Optimizing Cost
Derivative
Solve
Economic Lot Scheduling Single Item, Single Machine

## Slide 7: Optimal Lot Size
Total production
When unlimited production capabilities
  Economic Order Quantity (EOQ)
Economic Lot Scheduling Single Item, Single Machine

## Slide 8: Setup Time
Setup time s
If s  x(1-r) …lot size is optimal
Otherwise cycle length
is optimal
Economic Lot Scheduling Single Item, Single Machine

## Slide 9: Example
Production Q = 90/month
Demand D = 50/month
Setup cost c = $2000
Holding cost h = $20/item
Cycle time = 3 months
Lot size = 150 items
Idle time = 3(1-5/9)=1.33 months
Economic Lot Scheduling Single Item, Single Machine

## Slide 10: Example: Setup Times
Now assume setup time
If setup time < 1.33 months
  then 3 month cycle still optimal
Otherwise the cycle time must be longer
Economic Lot Scheduling Single Item, Single Machine

## Slide 11
Inventory
Month
Inventory
Month
1 2 3 4 5 6
1 2 3 4 5 6
s=1.3
s=2
Economic Lot Scheduling Single Item, Single Machine

## Slide 12: Multiple Items
Now assume n different items
Demand rate for item j is Dj
Production rate of item j is Qj
Setup independent of the sequence
Rotation schedule: single run of each item
  Cycle length determines the run length for each item
  Only need to determine the cycle length x
  Expression for total cost/time unit
Economic Lot Scheduling Multiple Items, Single Machine

## Slide 13
Average inventory level for the j-th item
Average total cost
Economic Lot Scheduling Multiple Items, Single Machine

## Slide 14: Optimal Lot-Size
Solve as before
Limiting case (infinite production rate)
Economic Lot Scheduling Multiple Items, Single Machine

## Slide 15: Feasibility check
Feasibility
 Q > D (demand can be met)
 D/Q < 1
  < 1 (=machine utilization)
When n>1:
Economic Lot Scheduling Multiple Items, Single Machine

## Slide 16: Example
Economic Lot Scheduling Multiple Items, Single Machine

## Slide 17: Solution
Economic Lot Scheduling Multiple Items, Single Machine

## Slide 18
The total average cost per time unit is
How can we do better than this?
Economic Lot Scheduling Multiple Items, Single Machine

## Slide 19: Setup Times
With sequence independent setup costs and no setup times the sequence within each lot does not matter
 Only a lot sizing problem
Even with setup times, if they are not job dependent then still only lot sizing
Economic Lot Scheduling Multiple Items, Single Machine

## Slide 20: Job Independent Setup Times
If sum of setup times < idle time then our optimal cycle length remains optimal
Otherwise we take it as small as possible
Economic Lot Scheduling Multiple Items, Single Machine

## Slide 21: Job Dependent Setup Times
Solution OK if: for any k , = idle time
Otherwise, there is a sequencing problem
Objective: minimize sum of setup times
in case of sequence dependent setup times, sjk minimized by solving corresponding TSP, denote minimum by T
Note: there are (n-1)! different sequences (rotation!!)
if then increase x until:
(i.e., machine is never idle)
Economic Lot Scheduling Multiple Items, Single Machine
Notes: TSP is NP hard
SST heuristic may also be applied

## Slide 22
sij = setup time between job i and job j
xij = 1 if “tour” visits i then j, and 0 otherwise (binary)
ti = arbitrary real numbers we need to solve for
An Integer Programming Formulation of the TSP

## Slide 23
Heuristics for the TSP
To apply the nearest-neighbor heuristic (NNH)
We begin at any city and then “visit” the nearest city.
Then we go to the unvisited city closest to the city we have most recently visited.
We continue in this fashion until a tour is obtained.
After applying this procedure beginning at each city, we take the best tour found.
In the cheapest-insertion heuristic (CIH)
We begin at any city and find its closest neighbor.
Then we create a subtour joining those two cities.
Next, we replace an arc in the subtour (say, arc (i, j) by the combinations of two arcs---(i, k) and (k, j), where k is not in the current subtour---that will increase the length of the subtour by the smallest (or cheapest) amount.
We continue with this procedure until a tour is obtained.
After applying this procedure beginning with each city, we take the best tour found.

## Slide 24: Example : sequence dependent setups
Optimal Sequence = 1-4-2-3
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 25: Arbitrary Cyclic Schedules
Sometimes a rotation schedule does not make sense
(remember problem with no setup cost)
For example, we might want to allow a cycle 1,4,2,4,3,4 if item 4 has no setup cost
No efficient algorithm exists
If sum of setups > idle time, then the optimal schedule has the property:
  Each machine is either producing or being setup for production
An extremely difficult problem with arbitrary setup times
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 26: Arbitrary Cyclic Schedules
Feasible solution exists if and only if:
(recall that: )
NP hard problem: no efficient algorithms
Define sequence as:
where: jk=k-th item in the sequence
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 27: Problem Formulation
Assume sequence-independent setup
Formulate as a nonlinear program
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 28: Notation
Setup cost and setup times
All possible sequences
Item k production in l-th position
Setup time s l, run time t l, and idle time u l
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 29: Inventory Cost
Let x be the cycle time
Let v be the time between beginning production of k
Total inventory cost for k is
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 30
The highest inventory level is: (Qk-Dk)tk  total inventory cost for k-th run:
ELSP formulation:
Meet demand for k
over cycle x
Meet demand k over v
(until k produced again)
Cycle length
Ik = all positions where
k is produced
Ll = all items produced
during v
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 31
ELSP master problem: sequence determination
ELSP subproblem: determination of cycle length, production & idle time
Frequency Fixing & Scheduling (FFS) heuristic
3 phases: 1. Computation of relative frequencies yk, and tk
2. Adjustment of relative frequencies  y’k, and t’k
3. Sequencing
Assumption:
the yk runs of item k are of equal length (tk), and evenly spaced
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 32: Optimal cycle, production and idle times subproblem
Subject to
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 33: Computing Relative Frequencies
Let yk denote the number of times item k is produced in a cycle
We will
  simplify the objective function by substituting
  drop the second constraint
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 34
Subject to
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule
Computation of relative frequencies yk, tk
Assume sequence that spaces production of item i uniformly over x

## Slide 35: FFS heuristic, phase 1: frequency fixing
Lagrange multiplier
Choose “appropriate”
x and determine the resulting yk’s
otherwise: =0
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule
Notes: Relaxatie door weglaten geheeltalligheidseisvan yk
Als gevolg blijft een model over met 1 set vergelijkingen. Vervolgens wordt hier een Lagrange relaxatie op uitgevoerd.
Merk op: indien geen setup time, dan valt Lagrange parameter weg!

## Slide 36: Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule
Finding λ using Newton’s method

## Slide 37: Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule
Power-of-2 adjustment for ti
  if all items produced in equal amounts and at equal time intervals, 2k policies optimal or near optimal.
  let B = length of base period (to be determined)
    key contribution of paper
  Goal : to have 2k adjustment to production “spacing” be close to x/yi
R. Roundy, “Rounding off to powers of 2 in continuous relaxations of capacitated lot sizing problems”,
Management Science, Vol. 35, No. 12, Dec. 1989, 1432-1441.

## Slide 38: FFS heuristic, phase 2: frequency adjustment
More approximate Power-of-2 adjustment for tk
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 39: FFS heuristic, phase 3: sequencing
Sequencing problem is equivalent to scheduling
jobs on ymax parallel machines, minimizing the makespan
Determine ymax=max(y1,…yn) = number of parallel machines
For each item k, there are yk jobs of length tk, evenly spaced, i.e.: when m=6, and yk=3, then there are two choices: assign the 3 jobs to (1,3,5) or to (2,4,6)
Use variant of LPT-heuristic to assign the jobs in decreasing order of yk, using tk as tie breaker, also in decreasing order
additional restriction that jobs must be evenly spaced
Concatenate the schedules of the ymax machines
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 40: Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule
“Bin packing” solution to production sequencing problem…minimizing the makespan on a set of parallel machines
Objective: space production of each item uniformly over time as possible
Example: suppose y1=23 y2=y3=22 y4=21 y5=20
  y1 determines number of bins to pack
  item 2 loaded before item 3 since t2>t3
  if loading of each bin equal… optimal
  but, adjustment of production times leads to suboptimal results
1 | 2 | 2 | 2 |  |  |  |  |  | 
1 | 3 | 3 | 4 | 4 | 4 | 4 |  |  | 
1 | 2 | 2 | 2 |  |  |  |  |  | 
1 | 3 | 3 |  |  |  |  |  |  | 
1 | 2 | 2 | 2 |  |  |  |  |  | 
1 | 3 | 3 | 4 | 4 | 4 | 4 |  |  | 
1 | 2 | 2 | 2 |  |  |  |  |  | 
1 | 3 | 3 | 5 | 5 | 5 | 5 | 5 |  | 

## Slide 41: Optimal cycle, production and idle times subproblem … with established item production in each position
Subject to
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule
substitute in objective function…
nonlinear “fractional program” results

## Slide 42: Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule
Recalculating the tk and uk , assuming production of item k is not equally spaced in the cycle
the item to be produced in each position of Ll is now known

## Slide 43: Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule
Item k production times and idle times update…

## Slide 44: FFS examples
1 machine, 4 items:
Items 1 2 3 4
Qj 400 400 500 400
Dj 50 50 60 60
hj 20 20 30 70
cj 2000 2500 800 0
sj 0.5 0.2 0.1 0.2
7.4.1: without setup times, x=2
7.4.2.: with setup times, x=3
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 45
20
40
60
80
100
Inventory
levels
0
0.5
1
1.5
2
time
Item3
Item3
Item1
Item2
Item4
FFS text example schedule for y’4=4
Economic Lot Scheduling Multiple Items, Single Machine, Arbitrary Schedule

## Slide 46
Have m identical machines in parallel
Setup cost only
Item process on only one machine
Assume
  rotation schedule
  equal cycle for all machines
Same as previous multi-item problem
Addition: assignment of items to machines
Objective: balance the load
Heuristic: LPT with
Economic Lot Scheduling Multiple Items, Parallel Machines

## Slide 47: Different Cycle Lengths
Objective: assign items to machines to balance the load
if cycle times are allowed to be different on the machines:
  calculate cycle time for each item, as if it were a single item model
  rank items in decreasing order of the cycle times
  Use sequence in ranking to fill machines as long as j<1
  NOTE: may lead to infeasible solution!  swapping
Complication: should not assign items that favor short cycle to the same machine as items that favor long cycle
Economic Lot Scheduling Multiple Items, Parallel Machines

## Slide 48
Model 1
  Assume no setup time
  Assume production rate of each item is identical for every machine
   Can be synchronized
  Reduces to single machine problem
2 machine case
  rotation schedules on both machines are the same
  there may be waiting times on machine 2 (machine 1 may wait)
  inventory costs remain the same; setup costs double
Economic Lot Scheduling Multiple Items, Flow Shop